## Slide 1: Engineering Case Studies (2)
Professor Bo Liu
James Watt School of Engineering

## Slide 2: Antenna design— antenna array design
What is the antenna array?
Multiple antennas working at the same frequency are fed and spatially arranged.
Directivity

## Slide 3: Antenna design— antenna array design
What is the circular antenna array?
The antennas are arranged in the form of rings.
For circular antenna array design, I=[I1,... , IN]T is the amplitude of array element feed current, β= [ β1,…, βN]T is the phase of the array element feed current. [I β]T are the design variables.

## Slide 4: Antenna design— antenna array design
Problem description
For circular antenna array, the design requirements include:
The sidelobe (SLL(x)) should not be more than -20 dB.
The directivity (D(x)) should not be less than 10 dB.
The gain (G(x) ) of θ =180° should not be less than – 0.1 dB for achieving the expected maximum radiation direction θ =180°.
G(x) of θ ∈ [80°~120°] should not be more than – 40 dB to nulling control the radiation in θ ∈ [80°~120°] .

## Slide 5: Antenna design— antenna array design
Problem description
However, the designer is not sure if the SLL(x) can meet –20 dB. If not meeting – 20 dB, he/she wants to see how small can it be and then decides the next step.

## Slide 6: Antenna design— antenna array design
Constrained optimization
How to formulate the problem into an optimization problem?
Constraints
Objective function
Design variables

## Slide 7: Antenna design— compact antenna design
What is the compact antenna?
Minimize the size.
What is the application of compact antenna?
Biomedical antenna (small size)
Satellite antenna (light weight)

## Slide 8: Antenna design— compact antenna design
Problem description
For the patch antenna, the design variables x=[a, b, d, kL, ds, dW, dWs, L0, Lg, Ls, Ws]. There are 2 design requirements.
The first objective is the magnitude of maximum return loss (|S11(x)|) smaller than -9 dB in the 4 GHz to 10 GHz operating band.
The second objective is the size of the antenna smaller than 400 mm2.
Even when meeting the requirements, the designer hopes to further optimize them.

## Slide 9: Antenna design— compact antenna design
Multi-objective optimization
Objective functions
Design variables
How to formulate the problem to an optimization problem?
s.t.
400 mm2
x=[a, b, d, kL, ds, dW, dWs, L0, Lg, Ls, Ws]
Inequality constraints

## Slide 10: Thanks!
#UofGWorldChangers
@UofGlasgow