## Slide 1: Use Particle Swarm Optimization via MATLAB: Engineering Case Studies
Professor Bo Liu
James Watt School of Engineering

## Slide 2: Design of a PID controller
Problem description
Proportional – Integral – Derivative (PID) control is widely used:
Controlling the temperature of a component
Controlling the elevation of a lift
Controlling the flight altitude and speed of unmanned aerial vehicle
PID
Controlled object
r(t)
e(t)
u(t)
y(t)
System output
Output of controller
Input of controller
Given error by the user
e(t)=r(t)-y(t)

## Slide 3: Hydraulic lift

## Slide 4: Design of a PID controller
Design requirement:
Minimize total error of control system
PID
Controlled object
r(t)
e(t)
u(t)
y(t)
e(t)=r(t)-y(t)
Determined by PID
Integral of error in t period
J(Kp, Ki, Kd)
is the control
objective.

## Slide 5: Design of a PID controller
The control system is built in Simulink (Hydraulic lift)

## Slide 6: Design of a PID controller
Optimization problem formulation
x=[Kp, Ki, Kd]
Kp ∈[20 80]
Ki ∈[1 5]
Kd ∈[1 100]
minimize J(x)

## Slide 7: Use PSO to find the optimal control parameters
Objective function in MATLAB
See live script
function [z] = PSO_PID(x)
% % Load the Simulink model and set the PID gains
load_system('Lift_PID');
assignin('base','Kp',x(1)); % Control parameter 1
assignin('base','Ki',x(2)); % Control parameter 2
assignin('base','Kd',x(3)); % Control parameter 3
out = sim('Lift_PID',[0,20]); % simulate the controller and the response is saved in info
info=stepinfo(simout.data);
disp(x)
z = 0.001*(info.RiseTime)+0.0006*(info.SettlingTime)+info.Overshoot+20*(abs(2-simout.Data(end))); % objective function to be minimized
%Weight coefficients in front of parameters are empirical
%the desired steady state is 2
end

## Slide 8: Use PSO to find the optimal control parameters
options = optimoptions('particleswarm','PlotFcn',@pswplotbestf,...
'SwarmSize',10,MaxIterations=20,UseParallel=false);
lb = [20 1 1];
ub = [80 5 100];
rng default
nvars = 3;
tic
[x, fval] = particleswarm (@PSO_PID,nvars,lb,ub,options)
toc
Perform PSO for finding the optimal x and objective function value

## Slide 9: Use PSO to find the optimal control parameters
Optimization process
See live script

## Slide 10: Use PSO to find the optimal control parameters
options = optimoptions('particleswarm','PlotFcn',@pswplotbestf,...
'SwarmSize',10,MaxIterations=20,UseParallel=true);
lb = [20 1 1];
ub = [80 5 100];
rng default
nvars = 3;
tic
[x, fval] = particleswarm (@PSO_PID,nvars,lb,ub,options)
toc
Perform PSO for finding the optimal x, objective function value and parallel computing
Parallel

## Slide 11: Use PSO to find the optimal control parameters
Optimization process
See live script

## Slide 12: Thanks!
#UofGWorldChangers
@UofGlasgow